# Precision and Accuracy
The NTP accuracy expectations depend on the environment and application requirements. In practice, the single factor most affecting accuracy at the longer update intervals used on global network paths is ambient temperature variations. Under typical room temperature conditions, the clock oscillator frequency can vary in the order of one part-per-million (PPM). This results in synchronization accuracy in the order of a few milliseconds at update intervals of fifteen minutes. However, accuracy can be much improved to the order of one millisecond at update intervals of one minute, as used with primary reference clocks.
At the lower update intervals, the primary factor affecting accuracy is jitter due to network and operating system latencies. With a GPS receiver and pulse-per-second (PPS) signal, together with operating system support in typical Unix kernels, the accuracy is in the order of a few microseconds. This of course is a property of the hardware and operating system, not the NTP protocol.
As a rule of thumb, the accuracy over the Internet is proportional to the propagation delay. For a lightly loaded 100-Mb/s Ethernet, the accuracy is in the order of 100 μs. For an intercontinental Internet path, the accuracy can be up to several tens of milliseconds.
On network paths with large asymmetric propagation delays, such as when one direction is via satellite and the other via landline, the errors can reach 100 ms or more. There is no way these errors can be avoided, unless there is prior knowledge of the path characteristics.

Master config (mine syncs to the NTP pool servers)
# /etc/ntp.conf, configuration for ntpd; see ntp.conf(5) for help
driftfile /var/lib/ntp/ntp.drift
# Enable this if you want statistics to be logged.
#statsdir /var/log/ntpstats/
statistics loopstats peerstats clockstats
filegen loopstats file loopstats type day enable
filegen peerstats file peerstats type day enable
filegen clockstats file clockstats type day enable
# Specify one or more NTP servers.
# Use servers from the NTP Pool Project. Approved by Ubuntu Technical Board
# on 2011-02-08 (LP: #104525). See http://www.pool.ntp.org/join.html for
# more information.
server 0.ubuntu.pool.ntp.org
server 1.ubuntu.pool.ntp.org
server 2.ubuntu.pool.ntp.org
server 3.ubuntu.pool.ntp.org
# Use Ubuntu's ntp server as a fallback.
server ntp.ubuntu.com
# Access control configuration; see /usr/share/doc/ntp-doc/html/accopt.html for
# details. The web page <http://support.ntp.org/bin/view/Support/AccessRestrictions>
# might also be helpful.
#
# Note that "restrict" applies to both servers and clients, so a configuration
# that might be intended to block requests from certain clients could also end
# up blocking replies from your own upstream servers.
# By default, exchange time with everybody, but don't allow configuration.
#restrict -4 default kod notrap nomodify query
#restrict -6 default kod notrap nomodify query
# Local users may interrogate the ntp server more closely.
restrict 127.0.0.1
restrict -6 ::1
# Clients from this (example!) subnet have unlimited access, but only if
# cryptographically authenticated.
restrict 192.168.1.0 mask 255.255.255.0
restrict -6 2001:pppp:pppp:pppp:: mask ffff:ffff:ffff:ffff::
# If you want to provide time to your local subnet, change the next line.
# (Again, the address is an example only.)
broadcast 192.168.1.255
broadcast ff05::101
multicastclient ff05::102
# If you want to listen to time broadcasts on your local subnet, de-comment the
# next lines. Please do this only if you trust everybody on the network!
#disable auth
#broadcastclient
Slave config
# /etc/ntp.conf, configuration for ntpd; see ntp.conf(5) for help
driftfile /var/lib/ntp/ntp.drift
# Enable this if you want statistics to be logged.
#statsdir /var/log/ntpstats/
statistics loopstats peerstats clockstats
filegen loopstats file loopstats type day enable
filegen peerstats file peerstats type day enable
filegen clockstats file clockstats type day enable
# You do need to talk to an NTP server or two (or three).
#server apollo.example.co.uk
server 192.168.1.11
#server 2001:pppp:pppp:pppp::1 # IPv6 local server
# pool.ntp.org maps to about 1000 low-stratum NTP servers. Your server will
# pick a different set every time it starts up. Please consider joining the
# pool: <http://www.pool.ntp.org/join.html>
#server 0.debian.pool.ntp.org iburst
#server 1.debian.pool.ntp.org iburst
#server 2.debian.pool.ntp.org iburst
#server 3.debian.pool.ntp.org iburst
# Access control configuration; see /usr/share/doc/ntp-doc/html/accopt.html for
# details. The web page <http://support.ntp.org/bin/view/Support/AccessRestrictions>
# might also be helpful.
#
# Note that "restrict" applies to both servers and clients, so a configuration
# that might be intended to block requests from certain clients could also end
# up blocking replies from your own upstream servers.
# By default, exchange time with everybody, but don't allow configuration.
restrict -4 default kod notrap nomodify nopeer noquery
restrict -6 default kod notrap nomodify nopeer noquery
# Local users may interrogate the ntp server more closely.
restrict 127.0.0.1
restrict ::1
# Clients from this (example!) subnet have unlimited access, but only if
# cryptographically authenticated.
#restrict 192.168.123.0 mask 255.255.255.0 notrust
# If you want to provide time to your local subnet, change the next line.
# (Again, the address is an example only.)
#broadcast 192.168.123.255
# If you want to listen to time broadcasts on your local subnet, de-comment the
# next lines. Please do this only if you trust everybody on the network!
disable auth
broadcastclient
multicastclient ff05::101
#manycastclient
On my network 192.168.1.11 (apollo) is the master clock, all other systems sync to apollo's NTP server. Make sure that the ntp server's firewall rules, if enabled, allow port 123 on both tcp and udp to the local subnet range and reboot ntpd service. Then just list your new ntp server in your other computer's /etc/ntp.conf server line.
Check that it's being used with the command
sudo ntpq -p
And your server should list a number in the "s" field (stratum) and it should be a lower number than 16, if you're getting 16 your server is not working as expected.
You can adjust the interval of "syncing" the time in the /etc/ntp.conf file (unfortunately under linux, with the default ntp configuration a time sync will happen every few seconds ~64s).
try to change the minpoll xxxx value to a high value (2^^xxxx)=seconds (6 = 64s) see Server Command Options
# /etc/ntp.conf
server 0.debian.pool.ntp.org minpoll xxxx maxpoll yyyy
server 1.debian.pool.ntp.org minpoll xxxx maxpoll yyyy
server 2.debian.pool.ntp.org minpoll xxxx maxpoll yyyy
server 3.debian.pool.ntp.org minpoll xxxx maxpoll yyyy
You can let act one RPi as local NTP server. but the local dhcp has to tell the other network devices that there is the RPi as ntp server. And even then, many devices are using its "hardcoded" timeservers - so they will ignore the existence of your local ntp server until you modify their configuration.
## NTP client

One of disadvantages designing so cheap computer is that you have to give up some features which are too expensive. One of these features is RTC - real-time clock. RTC chip has its own battery to store actual time even when device isn`t plugged in. This chip costs about 10$. This is quite ennough to persuade RPi designers to do not implement this feature.
Problem with storing actual time is partially solved by fake-hwclock package which writes actual time to text file every hour and at system reboot. At start, if no better source of time is present, time is set to one stored in that text file. Since RPi is disposing a RJ-45 port, we can use it as very precise time source within NTP. First we have to install package called ntp.
apt-get install ntp
Notice: The newer version of Raspbian have preinstalled timesyncd service. It can be used for the same purpose, but you can not have running both of them at the same time. To fix this you can stop and disable timesyncd service using these commands.
systemctl stop systemd-timesyncd
systemctl disable systemd-timesyncd
​/etc/init.d/ntp stop
​/etc/init.d/ntp start
Thats all, RPi is now synchronizing its time to NTP servers. By default it uses NTP servers which are generally too far from you. It has bad influence to time accuracy. So first go to page pool.ntp.org and find a location as near as possible. For me it is Czech Republic. To set NTP servers open ntp configuration file.
nano /etc/ntp.conf
And find lines starting with "server". Replace that lines for lines with servers from pool.ntp.org. In my case configuration looks like:
#/etc/ntp.conf, configuration for ntpd
driftfile /var/lib/ntp/ntp.drift
statsdir /var/log/ntpstats/
statistics loopstats peerstats clockstats
filegen loopstats file loopstats type day enable
filegen peerstats file peerstats type day enable
filegen clockstats file clockstats type day enable
# You do need to talk to an NTP server or two (or three).
#server ntp.your-provider.example
# pool.ntp.org maps to more than 300 low-stratum NTP servers.
# Your server will pick a different set every time it starts up.
# *** Please consider joining the pool! ***
# *** ***
server 0.cz.pool.ntp.org iburst
server 1.cz.pool.ntp.org iburst
server 2.cz.pool.ntp.org iburst
server 3.cz.pool.ntp.org iburst
# By default, exchange time with everybody, but don't allow configuration.
# See /usr/share/doc/ntp-doc/html/accopt.html for details.
restrict -4 default kod notrap nomodify nopeer noquery
restrict -6 default kod notrap nomodify nopeer noquery
# Local users may interrogate the ntp server more closely.
restrict 127.0.0.1
restrict ::1
# Clients from this (example!) subnet have unlimited access,
# but only if cryptographically authenticated
#restrict 192.168.123.0 mask 255.255.255.0 notrust
# If you want to provide time to your local subnet, change the next line.
# (Again, the address is an example only.)
#broadcast 192.168.123.255
# If you want to listen to time broadcasts on your local subnet,
# de-comment the next lines. Please do this only if you trust everybody
# on the network!
#disable auth
#broadcastclient
Now you can restart ntp service.
/etc/init.d/ntp restart
Here is command to check if time is synchronizing properly. To list NTP servers with which RPi is synchronizing:
ntpq -pn
You will get some output like this.
Remote	refid	st t	when	poll	reach	delay	offset	jitter
*81.27.192.20	195.113.144.238	2	u	26	64	1	58.571	0.797	68.634
+93.185.101.74	195.113.144.201	2	u	25	64	1	42.282	-1.507	0.477
+93.185.101.77	195.113.144.201	2	u	24	64	1	41.390	-1.544	68.243
-91.216.168.42	178.238.46.152	3	u	23	64	1	43.510	1.010	1.094
First letter have the most significant value of the table. * means actual time source, + means something like backup time source, - is ignored, but can become backup (+) at any time. First column shows IP adresses of NTP servers, second shows source of time for your NTP servers, third shows so called stratum. Stratum is number from 0 to 15 and shows number of hops from reference time (GPS clock, atomic clock...). That devices has stratum 0, but it is impossible to connect to them directly. For example, you have computer with sme kind of atomic clock conected (veeeery expensive - about 100 000$). Atomic clock box is stratum 0, your computer is stratum 1... Maybe you can also find stratum 16 which means untrusted time source. Column with "u" means that NTP server`s address is unicast. "When" indicates number of seconds passed since last response. "Poll" means interval between time requests, in seconds. "Reach" indicates success/failure to reach source. "Delay" indicates the roundtrip time, in milliseconds, to receive a reply. "Offset" is the difference between ntp server and your system clock in milliseconds. "Jitter" shows the difference, in milliseconds, between two samples.
Now you can check your time... I like to do everything in right way - so this command will print actual time in ISO 8601 (Representation of dates and times standard) format :)
date +"%FT%T%Z"
## NTP server
Now when RPi has synchronized its time, you can set it to pass this time information to devices in your local network. You only have to open configuration file of ntp daemon.
nano /etc/ntp.conf
And add a string that describes the hosts which requests will be answered.
restrict 192.168.1.0 mask 255.255.255.0
And also add this 2 lines. They will enable sending of broadcasts and multicasts containing time information for devices which accept them (Cisco, Juniper...)). Change first address in bold to broadcast address of your LAN. Do not change multicast address 224.0.1.1 since this addreess is assigned to NTP service by IANA and some network devices join this multicast group automatically.
broadcast 192.168.1.255
broadcast 224.0.1.1
Now close the configuration file (CTRL+X...) and save changes (...press "y" and Enter). Last step is to restart ntp daemon with:
/etc/init.d/ntp restart
From now you can configure machines in local network to synchronize its time to RPi. For example in Windows XP double click the clock in tray > Internet Time > check Automatically synchronize with an Internet time server and insert RPi`s IP address.

SNTP in Windows XP
First versions of Windows to Windows 8 still don`t have support for network time protocol. They use Simple network time protocol instead which have a limited accuracy. Accuracy is matter of up to 4 seconds which is much more than NTP`s few milliseconds :) SNTP in Windows synchronize the time once a week, NTP daemon in Debian synchronizes its time approximately every 512 seconds by default...